## Slide 1
Megaseries
11. Domain Controller cloning

## Slide 2: Prerequisites
Be sure to have a second domain controller already created that does not hold the PDC Emulator FSMO role (this one will be cloned)

## Slide 3: Support for Virtual Domain Controllers
Support for virtualizing Domain Controllers first appeared in Windows Server 2012

## Slide 4: Support for Virtual Domain Controllers
Support for virtualizing Domain Controllers first appeared in Windows Server 2012
It is possible thanks to a virtual device exposed at the hypervisor level that generates a unique ID

## Slide 5: Support for Virtual Domain Controllers
Support for virtualizing Domain Controllers first appeared in Windows Server 2012
It is possible thanks to a virtual device exposed at the hypervisor level that generates a unique ID
This ID changes at the Hypervisor level in case a snapshot is applied or a clone is made

## Slide 6: Support for Virtual Domain Controllers
Support for virtualizing Domain Controllers first appeared in Windows Server 2012
It is possible thanks to a virtual device exposed at the hypervisor level that generates a unique ID
This ID changes at the Hypervisor level in case a snapshot is applied or a clone is made
Any time a snapshot is applied on a DC or a DC is cloned then the Gen ID exposed by the hypervisor is compared to the one stored in Active Directory

## Slide 7: Domain Controller cloning
The reference domain controller has to be added to the Cloneable Domain Controllers group

## Slide 8: Domain Controller cloning
The reference domain controller has to be added to the Cloneable Domain Controllers group
In case you may have different software or roles installed that are not supported, an exclusion list has to be created

## Slide 9: Domain Controller cloning
The reference domain controller has to be added to the Cloneable Domain Controllers group
In case you may have different software or roles installed that are not supported, an exclusion list has to be created
Generate a clone config file

## Slide 10: Domain Controller cloning
The reference domain controller has to be added to the Cloneable Domain Controllers group
In case you may have different software or roles installed that are not supported, an exclusion list has to be created or the software or roles uninstalled
Generate a clone configuration file
Stop the reference VM and clone it. Start up the new machine and wait a couple of minutes for it to be available as a domain controller

## Slide 11: https://www.youtube.com/channel/UCcZ-jLbPwNr8E_v9-65n8Iw https://github.com/itknowledge4